## Slide 1: Source Estimation in Visual Experiments
David Kim
UCB/UCSF Bioengineering

## Slide 2
I. Background
II. Method
III. Results

## Slide 3
Background
II. Methods
III. Results

## Slide 4: Research Interest
Analyze visual experiments with non-invasive neuro-imaging for human subjects
  Accurate characterization of temporal response for each visual area

## Slide 5: Neuro-Imaging Techniques
Non-invasive techniques
  High temporal resolutions : EEG/MEG
  High spatial resolutions : MRI/fMRI

## Slide 6: Neuro-Imaging Techniques
Non-invasive techniques
  High temporal resolutions : EEG/MEG (msec)
  High spatial resolutions : MRI/fMRI

## Slide 7: Neuro-Imaging Techniques
Non-invasive techniques
  High temporal resolutions : EEG/MEG
  High spatial resolutions : MRI/fMRI (mm)

## Slide 8: Neuro-Imaging Techniques
Non-invasive techniques
  High temporal resolutions : EEG/MEG
  High spatial resolutions : MRI/fMRI

## Slide 9: Visual Information of Interest
  Basic Visual information include:
    Contrast / Luminance
    Orientation

## Slide 10: Visual Information of Interest
  Early Visual information include:
    Contrast / Luminance
    Orientation

## Slide 11: Visual Information of Interest
  Early Visual information include:
    Contrast / Luminance
    Orientation

## Slide 12: Early Visual Areas on Cortex
  Occipital Cortex
  Major Processing Areas
    V1
    V2
    V3

## Slide 13: Early Visual Areas on Cortex
  convoluted
  compact

## Slide 14: Early Visual Areas on Cortex
  convoluted
  compact

## Slide 15: Early Visual Areas on Cortex
  convoluted
  compact
  Source estimation becomes difficult
  }

## Slide 16: Challenges in visual expt: Resolving proximal sources
  Visual Field in 96 partitions
  Patch #93
  Patch #15
  1 cm

## Slide 17: Challenges in visual expt: Resolving convoluted sources
  1 cm
Because the occipital surfaces are highly folded, even small error in parameterization has large consequences at patch level.
4 mm shift
  #15 @ original position
  #15 @ shifted position

## Slide 18: Challenges in visual expt:
  1 cm
Trying to estimate source time functions from single patch experiment often results in highly variable time course.
Hagler et al. (2009)

## Slide 19
I. Background
Methods
III. Results

## Slide 20: Conceptual Approach (Crowd Sourcing)
Any single patch has some error associated as a result of noisy and misinformed model parameters
However, a larger ensemble dataset can effectively average out some of these errors when provided with additional appropriate constraints.

## Slide 21: Previous Works (Providing Additional Constraint)
  1. Common Response Assumption (CRA)
    When presented with identical stimuli, then cortical sources at similar eccentricities will respond identically

## Slide 22: Previous Works
  2. Common Topography Assumption (CTA)
    The cortical boundaries of activations are determined only by the boundaries of the stimulus. i.e stimulus contents have insignificant effects in determining cortical boundaries

## Slide 23: Source Estimation
  Typically, one generates a inversion operator W, that operates on the data such that the resulting estimation of time response minimizes some error estimate

## Slide 24: Source Estimation
  In typical single patch visual experiment, W is generated from forward model and relies heavily on the geometrical properties of the subject
  In our methods, we perform preliminary calibration experiments and use the resulting empirical ensemble data, to enhance W (resulting in an improved ensemble inverse operator, WE)

## Slide 25: Methods
f/MRI per patch
Sensor Config.
f/MRI per patch
Sensor Config.
96 patch Multifocal VEP
Typical Inverse
Generator
Empirical Inverse
Generator

## Slide 26: Source Estimation

## Slide 27
I. Background
II. Methods
Results

## Slide 28: Simulation & Results
Simulation Scenarios
  Ideal Conditions
    #, location, orientation of sources are accurate
  2. Error in geometry by MRI and segmentation
  Errors cortical orientations
  3. Error in source localization by fMRI
  Errors in cortical location
  4. Unaccounted external sources
  Errors in number of sources

## Slide 29: Simulation – Performance Test
20 Subjects * 32 Patches on peripheral rings
640 T1`
640 T2`
640 T3`

## Slide 30: Simulation – Performance Test
20 Subjects * 32 Patches on peripheral rings
640 T1`
640 T2`
640 T3`

## Slide 31: Simulation – Performance Test
Calculate correlations for each estimates per patch.
640 T1`
640 T2`
640 T3`
V1
V2
V3
Estimates , True
640 R1
640 R2
640 R3

## Slide 32: Simulation – Performance Test
Calculate correlations for each estimates per patch.
Some Data

## Slide 33: Scenario 1: Ideal Conditions
  For each patch, all relevant source characteristics are known and are accurate. All assumption holds.
Test | W | WE
1. Ideal | + | ?
2. Normal |  | 
2. Location |  | 
2. External |  | 

## Slide 34: Scenario 2: Error in Segmentation
What should have been used
for source analysis
(i.e. true directions of pyramidal cell organization that generates signal)
What was actually used for source analysis

## Slide 35: Scenario 2: Error in Segmentation
Test | W | WE
1. Ideal | + | ?
2. Normal | - | +
2. Location |  | 
2. External |  | 

## Slide 36: Scenario 3: Error in Localization
Due to some error in fMRI/MRI coregistration or misinterpretation of fMRI data, there are discrepancies between true source locations and assumed source locations
True Source Locations

## Slide 37: Scenario 3: Error in Localization
Due to some error in fMRI/MRI coregistration or misinterpretation of fMRI data, there are discrepancies between true source locations and assumed source locations
Assumed Source Locations

## Slide 38: Scenario 3: Error in Localization
Test | W | WE
3. Location |  | +

## Slide 39: Strengths and Weaknesses
Strengths:
  Gives inversion operator that can be used in human visual experiments which are typically challenging
  Very effective at eliminating wide variety of random errors
Weakness:
  There are many preliminary experiments that must be performed:
    Calibration multifocal VEP experiment
    f/MRI retinotopy
  Common Topography Assumption must be validated before WE can be used for single patch experiments that involve various stimuli

## Slide 40: Appendix

## Slide 41: Plausible Validation Experiment for CTA
f/MRI per patch
Sensor Config.
96 patch Multifocal VEP
Empirical Inverse
Generator
f/MRI per patch
Sensor Config.
48/96 patch Multifocal VEP
Empirical Inverse
Generator
f/MRI per patch
Sensor Config.
1/96 single patch VEP
Empirical Inverse
Generator
Many Patches
Single
Patch

## Slide 42: Scenario 4: Unaccounted External Source
  2 External Parietal Sources
    1.5 cm X 1.5 cm
    1. Constant: Constant amplitude, time-locked to stimulus
    2. Variable Amplitude across patches: Time-locked
    3. Variable Latency across patches: Constant amplitude

## Slide 43: Scenario 4: Unaccounted External Source
Test | W | WE
1. Ideal | + | ?
2. Normal | - | +
2. Location | - | +
2. External | - | +?

## Slide 44: Scenario 4: Unaccounted External Source
  PCA can be used to determine the number of contributing independent sources
  If the external sources are distant, spatial filtering methods like beam-forming can be used to isolate the contributions from distant sources
    Then run PCA to ascertain that maximum of 3 sources are active